## Slide 1: Table of Contents
Introduction
Construction
Studio Setting
Teaching Options
Lightboard setting
Lightboard teaching

## Slide 2: 1. Introduction
Technical lectures usually involve drawings and equations, drawn on chalkboards or whiteboards.
In capturing lectures on video however, the presenter must turn away from the audience to write or draw on the board, and the presenter’s body often obscures the material.
By using a Lightboard you can create visually compelling lectures and produce upload-ready videos with no post-production.
The Lightboard is a glass board, carrying light internally from LED strips along its edges. A video camera captures the presenter and his/her writing by viewing through the glass. The result is vivid, luminous writing floating in front of the presenter, who can now face toward the camera while drawing and interacting with the material on the board. The video is mirror-imaged on the fly to correct left-right reversal.
Notes: Herausforderung: Rekrutierung in der Fachlichkeit, obwohl gerade im FMB viele Externe Spezialisten Interesse haben, aufgrund der Vielfalt und des Purpose

## Slide 3: 2. Construction
  The lightboard is a 1,2m x 1,8m sheet of transparent plexiglass, 10.0 mm thick. The glass is lit internally from all four sides by bright white LEDs. Light travels to all parts of the glass by total internal reflection (TIR).
  The steel frame for the lightboard was produced by the mecanic faculty from LILAMA 2.
  You have to draw with fluorescent markers on the glass. The marks glow brightly due to their illumination via frustrated total internal reflection (FTIR) by light from inside the glass.

## Slide 4: 3. Studio Setting
    The media room in which "normal" video tutorials are filmed can also be used for recordings with the lightboard. The only difference: instead of a green back drop, a black back drop must be used.
    A video camera has to be mounted to the center of the Lightboard, about 5 to 6 meter away, viewing the presenter through the glass. The image is flipped horizontally.
    A monitor is placed just below the camera, in direct view of the presenter, to display the live stream of the video content being recorded. This afforded the presenter the ability to compose the video content in real-time.
    An additional computer can be used to display PowerPoint slides and other graphics.
    Video is saved as MPEG-4 video and is immediately available to the presenter.
Notes: In welchen Schritten kommen wir zu diesen Ergebnissen? Bspw. Beauftragung zur Entwicklung des Betriebsmodells

## Slide 5: 4. Teaching Options
  The Lightboard is a new presentation format, and it should dissuade instructors from simply replicating a classroom lecture in front of the camera. Instead, the content needs to be broken down into multiple segments, each being less than 10 minutes, and the instructor should consider utilizing the ability to combine written text and multi-media simultaneously.
  Videos created using the Lightboard can also be used for courses that are offered online, such as distance learning offerings and massive open online courses (MOOCs), for professional programs, and for remotely attending conferences
  Students can use the Lightboard to create videos for class presentations.
Notes: Insgesamt sind wir überzeugt, dass alle drei Szenarien Potential für eine moderne TZ bieten.
Für den weiteren Weg stehen für uns die Klärung einiger grundlegender Fragen und des Zielbildes im Vordergrund, Insbesondere geht es hier um diene Diskussion der Veränderung der Rolle der GIZ (vom technischen ebrater zum Provider von IT), Fragen der langfrostigen auftragsunabhänigen Finanzierung von IT Infrastruktur sowie der Verantwortung, in die wir uns als GIZ begeben, wenn wir Partner von uns abhängig machen.
Die Konzeptentwicklung konzentriert sich vor allem auf die gemeinsame Weiterentwicklung der Zielvorstellung mit allen Beteiligten im BMZ; sowie des langfristigen Betriebsmodells für atingi in allen drei Optionen und die damit einhergehenden kaufmännischen Fragen. Insebsondere müssen wir die

## Slide 6
Thank you for your attention!
Notes: atingi by default
Mehrwert für deutsche TZ
Offene Fragen zum Zielbild
…sind definiert
Optionen und Wachstumsszenarien und Marktanalyse sind erarbeitet
Umsetzung / Ausblick
Nächste Schritte